Poisson Solver
Nathan Chiu

---
Physics Engine
3D charge density
QM Simulator
Poisson Solver
Electrode properties
Material properties
Simulation parameters
3D Electric Potential

---
Purpose
QM simulator finds a 3D charge density based on initial assumptions on potential and state, sends it to Poisson Solver
- Poisson Solver finds a potential from 3D charge density, returns potential to QM simulator
- Repeat until convergence

---
I/O
- Inputs:
  - 3D volumetric charge density (including doping)
  - Electrode geometry and potentials
  - Material properties (workfunction, electron affinity, relative permittivity)
  - Simulation parameters (sample length, number of grid points, boundary condition type)
- Outputs:
  - 3D electrostatic potential

---
Algorithm
Initialize
(Define electrodes,
set sample parameters,
generate equation RHS)
Electrode
potential error
acceptable?
Done!
Call PoisFFT
Generate 3D potential
from electrode and charge
density information
Y
N
Apply correction to
charge density at
electrode surfaces

---
Examples (1):
- Periodic boundary condition
- Metre length scale
- 100x100x100 grid
- ~35 CPU seconds, ~11 wall clock seconds

---
Examples (2):
- Periodic boundary condition
- Metre length scale
- 100x100x100 grid
- ~50 CPU seconds, ~20 wall clock seconds

---
Examples (3):
- Periodic boundary condition
- Metre length scale
- 50x50x50 grid
- ~12 CPU seconds, ~5 wall clock seconds

---
Examples (4):
- Periodic boundary condition
- Micrometre length scale
- 200x200x200 grid
- ~1163 CPU seconds, ~360 wall clock seconds

---
Summary
- Iterative Poisson's equation solver using C++ FFT implementation
- Speed depends heavily on number of grid points and electrode placement complexity
- Parametrized in:
  - Physical material properties (permittivity, length)
  - Electrode properties (workfunction, electron affinity)
  - Simulation parameters (number of grid points, boundary condition type)